## Slide 1
Synthesis Features
  Task Driven Approach for simultaneous type and dimension synthesis*
  Synthesizes a planar four-bar linkage for Five or less Precision Poses
  Point and line constraints for fixed and moving pivots
  Reinterpretation of RR dyad
  Real-time tolerance based search for Circuit, branch and order defect Free Solution.
MotionGen: A Multi-touch app for Kinematic Design and Simulation of Linkages
Sit-to-Stand Motion
Prototype **
Hip lifting Motion
Shoulder lifting Motion
Real life device design
    A Novel Ge, Q. J., Zhao, P., and Purwar, A., 2013, “A Task Driven Approach to Unified Synthesis of Planar Four-bar Linkages using Algebraic Fitting of a Pencil of G manifolds”, ASME 2013 International Design Engineering Technical Conferences and Computers and Information in Engineering Conference, dETC2013-12977.
    ** Portable Six-Bar Apparatus For Lifting, Lowering and Self-Propelled Transit”, Inventors: Anurag Purwar et al, US Patent Application No. 12/868,446, 2010, awarded
Anurag Purwar, Jeffrey Ge, Mechanical Engineering
Synthesis
Simulation
Simulation and other Features
  Animation
  Coupler Point Path Simulation
  Linkage Classification
  Image Import
  Export in PDF and XML
  Imports .XML
Landing Gear Mechanism:
Three Poses with Moving Pivot Constraints
Excavator: Four Poses with Line Constraint for Fixed Pivots
Stamping Mechanism: Five Exact Poses
Simulation of Planar Four-Bar Film Advancing Mechanism